## Slide 1: ECE693H, Spring 2025: Multi-robot System Design
Dr. Daniel Drew
“Multi-robot Systems 2”

## Slide 2
MRS Survey Recap
A group ( >1 ) of robots with a common objective

## Slide 3
Questions?

## Slide 4
Class Overview
Lecture (~20 minutes)
Astound the Class (~40 minutes)

## Slide 5
Multi-robot Systems: Lecture 2 of 4
Lecture 1: MRS Survey
Lecture 2: Motion Planning
Lecture 3: Task Assignment (+Motion Planning if needed)
Lecture 3: Communication and Control Paradigms

## Slide 6
The Motion Planning Problem

## Slide 7
The Motion Planning Problem
What set of poses best gets the robot from A to B?

## Slide 8
Review of Single-Robot Motion Planning
Search-based
Sample-based
Where each position is
Notes: https://www.redblobgames.com/pathfinding/a-star/introduction.html

## Slide 9
Multi-robot Motion Planning: Taxonomies
Plan in the full (“global”) joint configuration space versus plan in individual (”local”) configuration spaces
(a) is an edge conflict, (b) a vertex conflict, (c) a following conflict, (d) a cycle conflict, and (e) a swapping conflict.
Search-based versus Sample-based
Coupled versus Decoupled
Conflicts
Same dichotomy!

## Slide 10
Single Robot Planning: A*

## Slide 11
Single Robot Planning: A*

## Slide 12
Single Robot Planning: A*
We can make choices about where nodes and edges go (e.g., doors)

## Slide 13
Single Robot Planning: A*
We can make choices about grid resolution

## Slide 14
Single Robot Planning: A*
https://www.redblobgames.com/pathfinding/a-star/introduction.html

## Slide 15
Search-based Methods for MRS

## Slide 16
A* with Replanning: Local Repair (LRA*)

## Slide 17
A* with Replanning: Local Repair (LRA*)
Don’t need to replan the entire route

## Slide 18
A* with Replanning: Local Repair (LRA*)
Local replanning without additional rules leads to collision cycles.
One workaround: “agitation”: after a cycle, add random noise to the graph edges.

## Slide 19
Cooperative A* (CA*)
Add command
Challenge: curse of dimensionality

## Slide 20
Conflict Based Search (CBS)
Constraint (agent can’t occupy vertex at time)
Conflict (agent 1 and 2 occupy vertex at time)

## Slide 21
A* Recap Video

## Slide 22
D* and D* Lite
Two separate lists maintained:
“G” score = Cost to connect the starting point to the current point
“RHS” score = Connection cost from current node to next node, inf. for obstacle; aka one-step lookahead cost
when G(s) /=/ RHS(s), queue for update.

## Slide 23
D* and D* Lite
Initial plan
Obstacle encountered

## Slide 24
D* and D* Lite
Obstacle encountered
Plan updated

## Slide 25
D* and D* Lite

## Slide 26
Contrasting These Approaches
A* with replanning:
Initial planning: A*
Replanning: Re-run A*
Efficiency: Poor
Optimality: High
D* Lite:
Initial planning: A*-ish in reverse
Replanning: Update lookahead cost RHS(s)
Efficiency: High
Optimality: Variable
D* Lite for mostly dynamic environments, A* for mostly static

## Slide 27
Single Robot Planning: Sampling-based Methods
What do we do if we have no grid, or the required grid dimensions make computation infeasible, or we have many degrees of freedom?
Succinctly: Sampling-based methods are good for large-scale, continuous environments with high-dimensional robots

## Slide 28
Single Robot Planning: Probabilistic Roadmap (PRM)

## Slide 29
Single Robot Planning: PRM

## Slide 30
Single Robot Planning: PRM

## Slide 31
Single Robot Planning: PRM

## Slide 32
Single Robot Planning: RRT
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378
Initial position
Target position
Instead of a discretized grid, positions are sampled from the continuous state space
(grid in images shown for visualization only)

## Slide 33
Single Robot Planning: RRT
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378
Points are added to the “tree”, then checked for 1) collisions with obstacles, 2) collisions with obstacles between nodes

## Slide 34
Single Robot Planning: RRT
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378
Valid path formed to target
Path can be “smoothed” by re-sampling between path points

## Slide 35
Single Robot Planning: RRT
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378
Find the nearest node in tree
Generate a new node in direction of sampled node
Collision check
Add new node to tree
Return status (reached/advanced/trapped)

## Slide 36
Single Robot Planning: RRT
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378

## Slide 37
Single Robot Planning: RRT*
https://theclassytim.medium.com/robotic-path-planning-rrt-and-rrt-212319121378
Continuously “rewire” the graph based on closest vertices
Find the nearest node in tree
Generate a new node in direction of sampled node
Collision check
Check whether new node is closer to any existing nodes
Rewire tree to result in lowest total cost path

## Slide 38
Single Robot Planning: RRT Visualized

## Slide 39
Single Robot Planning: RRT* Visualized

## Slide 40
Multi-Agent RRT (MA-RRT*)
(first extend RRT* with G-RRT*, which discretizes state space into a motion graph; when expanding from start, still samples points randomly, then uses graph-based search to find optimal path)
State space:
where is waypoint of agent 1;
waypoint includes time
Distance between two joint spaces:
Then consider:
(obviously, this hurts our spatial intuition)

## Slide 41
Discrete RRT (dRRT / dRRT*)
First compute individual optimal roadmaps using G-RRT*
THEN sample from joint configuration space of the roadmaps
Why? The joint configuration space is highly dimensional; faster to solve individual roadmaps then only sample and replan from those “good” solutions

## Slide 42
Decentralized RRT (dRRT*)

## Slide 43
Quick Summary
For scenarios with an omniscient planner: A* is ubiquitous (e.g., video games)
For highly dynamic environments: D*-lite is state of the art
For large, high-dimensional state spaces: dRRT* is state of the art
Multi-agent coordination: D*-lite does not explicitly account for other robots!
Common approach: “prioritized planning”, where high-priority robots maintain their path, low-priority robots must replan.

## Slide 44
Questions?
Questions?
Lecture (~20 minutes)
Subsystem check-in (~40 minutes)
Lecture 1: MRS Survey
Lecture 2: Motion Planning
Lecture 3: Task Assignment (+Motion Planning if needed)
Lecture 3: Communication and Control Paradigms

## Slide 45
693H Robotic Subsystems
-Second Design Review Presentations are 3/10, 3/12
-You will be expected to have functional prototypes complete to show by then
-You will be expected to have PCB designs and final BoMs complete by then