## Slide 1: ECE693H, Spring 2025: Multi-robot System Design
Dr. Daniel Drew
“Multi-robot Systems 2”

## Slide 2
MRS Motion Planning Recap
For scenarios with an omniscient planner: A* is ubiquitous (e.g., video games)
For highly dynamic environments: D*-lite is state of the art
For large, high-dimensional state spaces: dRRT* is state of the art

## Slide 3
Questions?

## Slide 4
Class Overview
Lecture (~40 minutes)
Subsystem checkins (~20 minutes)

## Slide 5
Multi-robot Systems: Lecture 3 of 4
Lecture 1: MRS Survey
Lecture 2: Motion Planning
Lecture 3: Task Assignment (+Motion Planning if needed)
Lecture 4: Communication and Control Paradigms

## Slide 6
Task Assignment Examples

## Slide 7
The Task Assignment Problem
The Multi-robot Task Assignment (MRTA) problem: assign set of robots to a set of tasks such that overall performance is optimized by some metric(s), subject to some set of constraints
, the set of robot utilities, where is the utility of robot i to execute task j

## Slide 8
Task Assignment: Taxonomies
Instantaneous: Decisions made only based on current state
Time-extended: Planning over a finite time horizon
Offline: Assignments and planning done based on simulation / model
Online: Assignments and planning dynamically adjusted

## Slide 9
Task Assignment: Taxonomies

## Slide 10
Task Assignment: Two Major Paradigms
“Hungarian Algorithm”
Market-based Allocation
(various approaches)
CENTRALIZED
DECENTRALIZED
Approaches we will talk about later in the context of swarms:
Genetic algorithms, ant colony optimization
Approaches we will not talk about:
Centralized, math-intensive (e.g., mixed-integer linear programming and other multi-factor optimization methods)

## Slide 11
The Hungarian Algorithm (HA)
Inputs:
Number of robots n and number of tasks m
Cost matrix C, an n x m matrix (often padded to be square)
Cost metric definition for
Examples of cost metrics:
-Travel time or distance
-Energy consumption
-Execution time
-Task priority
Constraints on C for typical HA:
-Finite, comparable values
-Non-negative costs
-Independence of costs (e.g., cost should not depend on other assignments)

## Slide 12
The Hungarian Algorithm (HA)

## Slide 13
The Hungarian Algorithm (HA)
(reminder: big O notation describes how run time scales as input grows)

## Slide 14
Task Assignment: Taxonomies

## Slide 15
Market-based Assignment
Key Assumptions:
Robot revenue is a combination of personal and system profit
Robots work to maximize revenue
Robots are honest with eachother
Based on the “Efficient Market Hypothesis” (an important basis for capitalism), this will result in near-optimal solutions to task prices.

## Slide 16
Market-based Assignment: Single Task Trades

## Slide 17
Market-based Assignment: Single Task Trades

## Slide 18
Market-based Assignment: Single Task Trades

## Slide 19
Market-based Assignment: Complex Tasks  Task Trees

## Slide 20
Market-based Assignment: Complex Tasks  Task Trees

## Slide 21
Market-based Assignment: Complex Tasks  Task Trees

## Slide 22
Market-based Assignment: Complex Tasks  Task Trees

## Slide 23
Market-based Assignment: Complex Tasks  Task Trees

## Slide 24
Market-based Assignment: TraderBots
Consider a team of robots assembled to perform a set of tasks in a dynamic environment. Consider further, that the team of robots is modeled as an economy, and each robot in the team is modeled as a self-interested trader in this economy. Thus, the goal of the team is to complete the tasks successfully while maximizing overall profits (i.e. the difference between revenue and cost), while each robot will aim to maximize its individual profit. Thus, robots will hold auctions and submit bids to determine task allocations within the team, and the different tasks and information will be the commodities traded in the economy. A system such as this will inherit many desirable characteristics from the market methodology. The competitive element of the robots bidding for different tasks enables the system to decipher the competing local information of each robot (note that there is no central agent evaluating information and planning for the entire system), while the common currency provides grounding for the competing local costs in relation to the global priorities/value of the tasks being performed

## Slide 25
Market-based Assignment: TraderBots

## Slide 26
Contrasting These Approaches
Agent count scalability (computation)
Communication challenges (network scaling, single point of failure)
Complex task interdependency (constraints on cost metric for HA)
When to use decentralized market-based approaches?
How to choose between all the market-based approaches?
How do tasks arrive?
Number of robots and tasks?
MRS composition?
Optimality vs speed?

## Slide 27
Contrasting These Approaches

## Slide 28
Standard solutions?
Unlike for motion planning (e.g., with Nav2), there is no standard solution to MRTA in ROS2.
Exercise for you to think about: What would this look like?
Note: HA and fully centralized approaches are “easy” to implement.

## Slide 29
Questions?
Questions?
Lecture (~40 minutes)
Subsystem check-in (~20 minutes)
Lecture 1: MRS Survey
Lecture 2: Motion Planning
Lecture 3: Task Assignment (+Motion Planning if needed)
Lecture 4: Communication and Control Paradigms

## Slide 30
693H Robotic Subsystems
-Second Design Review Presentations are 3/10, 3/12
-You will be expected to have functional prototypes complete to show by then
-You will be expected to have PCB designs and final BoMs complete by then