## Slide 1: ECE693H, Spring 2025: Multi-robot System Design
Dr. Daniel Drew
“Action 1”

## Slide 2
Week 1 Recap
Action
Perception
Intelligence
(not just sensing)
(not just moving)
(not just classification)
Off-the-shelf research platforms let you work at high levels of the stack while abstracting out things like:

## Slide 3
Swarm-on-a-Stick
We will create an open-source swarm robotics kit for education, from scratch.

## Slide 4
693H Robotic Subsystems
Control and Planning
Perception
Compute and Power
Mobility
Motors, drive electronics, encoders, PID controllers, top-down tracking
Sensor suite (IMU, prox.), calibration code, general IO (buttons and LEDs)
microROS, ROS2, Gazebo simulation, enclosure design
Battery and charging, wireless comms, GPIO and power distribution routing
Mechanics / Prototyping
Coding
PCB Design

## Slide 5
Questions?

## Slide 6
Welcoming New Students
Please share:
Your name and grade level (e.g., ECE senior)
How you heard about this course
What you're excited about in this course
What you're worried about with this course (e.g., technical content, not enough programming experience)
Are neither, one, or both of these examples of robots?
What makes something a robot?

## Slide 7
Class Overview
Lecture (~40 minutes)
Subsystem check-in (~5 minutes only)
FabLab training (~4:15pm)

## Slide 8
Action: Lecture 1 of 2
Lecture 1: motors  encoders
Lecture 2: motor control  motion planning

## Slide 9
Lecture Overview: Ascending the Stack
Electromagnetic motors
Motor gearing and mechanics
Motor driver electronics
Encoders

## Slide 10
Electromagnetic Motors: Types and Examples

## Slide 11
Electromagnetic Motors: Basic Physics
Lorentz force
(curl right hand rule for electromagnets)
microscopic
macroscopic, net force on current-carrying conductor
Ampere-Maxwell Law

## Slide 12
Electromagnetic Motors: Basic Physics
steady state velocity
armature current
armature torque
full equation of motion
“back emf” constant
motor torque constant

## Slide 13
Electromagnetic Motors: Brushed DC Motor
7:10

## Slide 14
Electromagnetic Motors: Brushed vs Brushless

## Slide 15
Electromagnetic Motors: Brushless DC Motor
2:40

## Slide 16
Electromagnetic Motors: Brushed vs Brushless
Rotor vs stator: In brushed motors, the rotor has the electromagnet and the stator has permanent magnets. Brushless are the opposite.
Physical contact vs control complexity: Brushed motors use physical contact for commutation. Brushless motors require electronic controller to time the switching.
High performance vs cost and integration simplicity: Brushless motors are better by every metric, but are more expensive and more complex to integrate.
Brushed
Brushless

## Slide 17
Electromagnetic Motors: Servos
DC motor
RC servo

## Slide 18
Electromagnetic Motors: Servos
RC servo
flap control
steering
main drive
(continuous servo)

## Slide 19
Electromagnetic Motors: Servos
typical use
what’s actually happening?
but what’s ACTUALLY happening?

## Slide 20
Electromagnetic Motors: Servos
4:10

## Slide 21
Servo Hacking
as seen in…

## Slide 22
Electromagnetic Motors: Steppers
very small step sizes, high torque, “easy” to control precisely, relatively cheap for performance you get

## Slide 23
Electromagnetic Motors: Steppers
5:11

## Slide 24
DC Motor Gearing
(recommended to operate dc motor at no more than 25% of stall current)

## Slide 25
DC Motor Gearing
No load speed：6600rpm
Stall current：0.8A。
Torque requirement for 500g robot, driving 0.5m/s, with 2.5cm radius wheels, is on the order of 13mNm at ~200RPM

## Slide 26
DC Motor Gearing
Stall current = ~10x hobby motor
Max eff. torque / 10 = 0.5mNm
6600 RPM / 48 = ~140 RPM
0.5mNm * 48 = ~24 mNm
25% of 24 = 6mNm
Two motors => 12mNm total torque
Torque requirement for 500g robot,
driving 0.5m/s, with 2.5cm radius wheels,
is on the order of 13mNm at ~200RPM
No load speed：6600rpm
Stall current：0.8A。
1:48 gear ratio

## Slide 27
Motor Drivers: H-Bridges – Motivation
How would we power the motor?

## Slide 28
Motor Drivers: H-Bridges – What and Why
Build up to h bridge components one by one
4:36

## Slide 29
Motor Drivers: H-Bridges at a High Level
2:45

## Slide 30
Encoders: Integration and Use
Vehicle position
Wheel speed
Vehicle heading angular velocity
Incremental encoders are typical for mobility
Quadrature encoders give direction

## Slide 31
Encoders: Integration and Use
1:120 TT motor
Magnetic quadrature encoder
Integrated
Hall effect sensors

## Slide 32
Encoders: Integration and Use
Counts per revolution of wheel shaft: CPR * gear ratio
To calculate RPM: counts since last read / delta t
e.g.,
counts = encoder.counts – last_counts
countspersec = counts / deltat
rpm = countspersec * (60 / (12*120))
“12 CPR”

## Slide 33
Questions?
Questions?
Lecture 1: motors  encoders
Lecture 2: motor control  motion planning
Lecture (~40 minutes)
Subsystem check-in (~5 minutes only)
FabLab training (~4:15pm)

## Slide 34
693H Robotic Subsystems
Control and Planning
Perception
Compute and Power
Mobility
Motors, drive electronics, encoders, PID controllers, top-down tracking
Sensor suite (IMU, prox.), calibration code, general IO (buttons and LEDs)
microROS, ROS2, Gazebo simulation, enclosure design
Battery and charging, wireless comms, GPIO and power distribution routing
Mechanics / Prototyping
Coding
PCB Design