## Slide 1: ECE693H, Spring 2025: Multi-robot System Design
Dr. Daniel Drew
“Perception 1”

## Slide 2
Action Recap
Electromagnetic motors
Motor gearing and mechanics
Motor driver electronics
Encoders
Action
Ascending the stack from the motor
Localization / Odometry
Path and Motion Planning

## Slide 3
Action: End-to-End Overview
Path Planning
series of poses
Kinematics
desired
Odometry
Encoder
Motor
Wheel
physical
parameters

## Slide 4
Action: End-to-End Overview
Path Planning
series of poses
Kinematics / Odometry
What about speed?
Easiest thing to do / assume: constant linear velocity

## Slide 5
Questions?

## Slide 6
Class Overview
Lecture (~50 minutes)
Subsystem check-in (~15 minutes)

## Slide 7
Perception: Lecture 1 of 2
Lecture 1: sensors  data acquisition
Lecture 2: signal processing  mapping

## Slide 8
Lecture Overview: Ascending the Stack
Overview / Taxonomy
Sensor physics
Data acquisition

## Slide 9
Sensors: Types and Examples
CLASS
QUANTITY
NAME
Passive
Intensity
Pressure
Image
Deflection
Microphone
Camera
Altimeter /
Barometer
IMU
Active
Distance
Time-of-flight,
received angle/intensity
LiDAR
Ultrasonic
Infrared

## Slide 10
Sensors: Optical Time-of-Flight
Light Detection and Ranging

## Slide 11
Sensors: Optical Time-of-Flight
3:15

## Slide 12
Sensors: Optical Non-ToF
Photodiode

## Slide 13
Sensors: Optical Non-ToF
3:00

## Slide 14
Sensors: Acoustic Time-of-Flight
HC-SR04 (common)

## Slide 15
Sensors: Acoustic Time-of-Flight
4:20

## Slide 16
Interlude: Micro Electromechanical Systems (MEMS)

## Slide 17
Interlude: Micro Electromechanical Systems (MEMS)

## Slide 18
Interlude: Micro Electromechanical Systems (MEMS)
2:05

## Slide 19
Sensors: Barometer / Altimeter
Piezoresistive Pressure Sensor
Capacitive Pressure Sensor

## Slide 20
Sensors: Barometer / Altimeter
Piezoresistive Pressure Sensor
Barometer-based altimetry accurate to a few meters

## Slide 21
Sensors: Barometer / Altimeter
Piezoresistive Pressure Sensor
Barometer-based altimetry accurate to a few meters
Note: small altimeters are usually optical tof, not pressure;
they fly low enough to not need a barometer

## Slide 22
Sensors: Barometer / Altimeter

## Slide 23
Sensors: Microphones
Electret microphone
Electret materials have a permanent static charge, so capacitor doesn’t need to be externally powered

## Slide 24
Sensors: Microphones

## Slide 25
Sensors: Microphones
Inan et al., 2017
Common in mobile devices (e.g., smartphones)

## Slide 26
Sensors: MEMS Inertial Measurement Unit
“6-axis IMU” = Accelerometer, gyroscope. “9-axis IMU” = Accel., gyro., compass
Accelerometer
Gyroscope

## Slide 27
Sensors: MEMS Inertial Measurement Unit
Accelerometer

## Slide 28
Sensors: MEMS Inertial Measurement Unit

## Slide 30
Sensors: Cameras

## Slide 31
Sensors: Cameras
2:05

## Slide 32
Lecture Overview: Ascending the Stack
Overview / Taxonomy
Sensor physics
Data acquisition
Many sensors involve a TRANSDUCTION from the physical quantity to a change in resistance, capacitance, or stored charge
How do we turn this into data in our computer?

## Slide 33
Readout Circuitry: Wheatstone Bridge
Many transducers output a change in resistance:
e.g., piezoresistive pressure sensors, strain gauges, load cells, thermocouples
Wheatstone bridges can:
-Increase sensitivity
-Compensate for environmental factors
-Allow for fully differential measurement

## Slide 34
Readout Circuitry: Wheatstone Bridge
5:14

## Slide 35
Readout Circuitry: Op. and Inst. Amplifiers
WHY USE AN AMPLIFIER?
Typical voltage output of a strain sensor is mV
Mainly interested in differential signals (e.g., Wheatstone bridge)
Prevent loading of sensor circuit
e.g., piezoelectric sensors, microphones, strain gauges, thermocouples
Infinite open-loop gain, infinite input impedance, voltage difference between inputs is zero
op-amp in negative feedback

## Slide 36
Analog-to-Digital Conversion: Basic Concept
Output of sensor readout circuits is (almost always) an analog voltage
How do we convert this into something readable by a computer? (digital info)
“3-bit” ADC:
000 to 111 in binary
0 to 7 in decimal
“full-scale”
(typ. VCC of ADC)
Either built into your microcontroller (e.g., ESP32)
OR purchased as discrete IC (only when needed)
e.g., Successive Approximation Register (SAR)
Delta-Sigma, Flash
Resolution =

## Slide 37
Analog-to-Digital Conversion: Video
4:50

## Slide 38
Questions?
Questions?
Lecture (~50 minutes)
Subsystem check-in (~15 minutes)
Lecture 1: sensors  data acquisition
Lecture 2: signal processing  mapping

## Slide 39
693H Robotic Subsystems
REMINDERS:
-PARTS ORDER DUE 2/3
-First Design Review Presentations are 2/10, 2/12
-I will randomly select which two groups present which day. Be ready on 2/10.
-Poll: DIY Powerpoints or Google Slides with (loose) templating?